## Slide 1: NSG Pilkington – University of Liverpool Machine Learning Project: 18/11/2020
Dr. Peter Green
Diego Echeverria
Risk Institute,
School of Engineering

## Slide 2
To-do (short-term)
Need bespoke filtering for some of the signals (we can do this with an extra column in the spreadsheet).
Establish and implement strategy for processing data that is affected by reversals.
Run the pre-processing tasks defined in the flow chart with the 168 inputs specified in the spreadsheet “UK5 AI Furnace Model Input Pre-Processing”.
To-do (longer-term)
Repeat analysis that use randomly selected inputs and/or randomly selected time lags.
Consider using a multi-output linear regression.

## Slide 3
Pre-processing the inputs affected by the reversals process
Most of the inputs associated with the reversals were set to 1 for low-pass filtering in the “Model Input Pre-Processing 20201109” file.
After the 11 Nov 2020 meeting, it was recommended that we should not applied a low-pass filter because the input’s signal (identified with the reversals) were not affected by measurement noise.
Therefore, we created a change log-file ‘Model Input Pre-Processing 20201112’ where we set the low-pass filter to 0 for the inputs affected by the reversals.
We use ‘Model Input Pre-Processing 20201112’ file for the following pre-processing tasks.

## Slide 4
Pre-processing the inputs affected by the reversals process
Zoom in

## Slide 5: Pre-processing the inputs affected by the reversals process
Contains spikes?
High pass filter
Remove spikes
Apply reversals processing?
Reversals
strategy
Does it require low-pass filtering?
Filter
Interpolate
Yes
Yes
Yes
No
No
No
To create pipeline 6

## Slide 6
Strategy for processing data that is affected by the reversals
Use the standard deviation of the maximum values with a 20-minute time period
Start data processing at the minimum value of the first 20 minutes:
  We search for the minimum value of the signal at the first 20 minutes to identify the point before the next firing.
Identify the maximum value within a 20-minute time period.
Get the signal values within around the maximum value.

## Slide 7
Strategy for processing data that is affected by the reversals

## Slide 8
Strategy for processing data that is affected by the reversals
Zoom in

## Slide 9
Strategy for processing data that is affected by the reversals
Starting point
* Within
Max values

## Slide 10
Strategy for processing data that is affected by the reversals
2) Use the standard deviation of the maximum values with a 20-minute time period
Start data processing at the minimum value of the first 20 minutes:
  We search for the minimum value of the signal at the first 20 minutes to identify the point before the next firing.
Identify the maximum value within a 20-minute time period.
Get the signal values within around the maximum value.
  We can introduce a parameter to control the range where the values are captured.
  We can change to have more inclusive bounds.

## Slide 11
Online linear regression using data affected by the reversals: Rectified
Pipeline | Av. RMSE
1 | 4.59
2 | 4.70
3 | 4.31
4 | 4.30
5 | 4.31
6 | 4.50

## Slide 12
Time lags
Linear regression
Remove inputs with low importance
Model parameters
Data processing
Machine learning
To create pipeline 7

## Slide 13
Online linear regression eliminating non-relevant tags
Inputs whose weights were always below 10%:
10279 Canal Temp Control (PV) - Also a pyromter
15119 Furnace Pressure (PV)
321 Glass Level Control (PV)
6463 Main Gas Pressure (PV)
7483 Open Crown Temperature - Port 6 (PV)
6585 Port 6 Gas Flow (PV)

## Slide 14
Retained inputs:
10425 Calculated Cullet Ratio
1950 Canal Temp Control Pyrometer (2)
10278 Canal Temp Control (OP)
2918 Closed Bottom Temperature - Port 6 (PV)
2921 Closed Bottom Temperature - Upstream Working End (PV)
1650 Combustion Air Temperature Measurement
2911 Filling Pocket Closed Bottom Temperature LHS (PV)
11201 Furnace & Services Pack Sub S8 L.H. Section - HV13
11204 Furnace & Services Pack Sub S8 R.H. Section - HV16
11174 Furnace Bottom Temperature 18m DS of B8
10091 Furnace Load ? (t w)
9403 Furnace Pressure (OP)
9393 Glass Level Control (OP)
7474 Lehr Drive Line Shaft Speed
7746 Open Crown Temperature - Port 2 (PV)
7522 Open Crown Temperature - Port 4 (PV)
7525 Open Crown Temperature - Port 7 (PV)
7999 Outside Windspeed Anemometer
11105 Port 1 Combustion Air Flow LHS (OP)
11111 Port 2 - 3 Combustion Air Flow LHS (OP)
8390 Port 5 Gas Flow (PV)
7667 Port 7 Gas Flow (PV)
11221 Services Building MCC1 - MV67
11217 Services Building MCC9 Cat B Supply - MV60
8344 Total CCCW Flow Measurement
136 Total Combustion Air Flow Measurement
135 Total Firm Gas Flow Measurement
9282 Tweel Position
30060 U S Flowing End Air Flow Measurement
11384 Wobbe Index (Incoming Gas)
Online linear regression eliminating non-relevant tags

## Slide 15
Online linear regression using data affected with the reversals, rectified and filtered
Pipeline | Av. RMSE
1 | 4.59
2 | 4.70
3 | 4.31
4 | 4.30
5 | 4.31
6 | 4.50
7 | 4.27

## Slide 16: Pre-processing the inputs affected by the reversals process
Contains spikes?
High pass filter
Remove spikes
Apply reversals processing?
Reversals
strategy
Does it require low-pass filtering?
Filter
Interpolate
Yes
Yes
Yes
No
No
No
To create pipeline 8

## Slide 17
Pipeline | Av. RMSE
1 | 4.59
2 | 4.70
3 | 4.31
4 | 4.30
5 | 4.31
6 | 4.50
7 | 4.27
8 | 4.25
Online linear regression using data affected with the reversals: Rectified and filtered

## Slide 18
Time lags
Linear regression
Remove inputs with low importance
Model parameters
Data processing
Machine learning
To create pipeline 9

## Slide 19
Online linear regression eliminating non-relevant tags
Inputs whose weights were always below 10%:
10279 Canal Temp Control (PV) - Also a pyromter
15119 Furnace Pressure (PV)
321 Glass Level Control (PV)
6463 Main Gas Pressure (PV)

## Slide 20
Retained inputs:
10425 Calculated Cullet Ratio
1950 Canal Temp Control Pyrometer (2)
10278 Canal Temp Control (OP)
2918 Closed Bottom Temperature - Port 6 (PV)
2921 Closed Bottom Temperature - Upstream Working End (PV)
1650 Combustion Air Temperature Measurement
2911 Filling Pocket Closed Bottom Temperature LHS (PV)
11201 Furnace & Services Pack Sub S8 L.H. Section - HV13
11204 Furnace & Services Pack Sub S8 R.H. Section - HV16
11174 Furnace Bottom Temperature 18m DS of B8
10091 Furnace Load ? (t w)
9403 Furnace Pressure (OP)
9393 Glass Level Control (OP)
7474 Lehr Drive Line Shaft Speed
7746 Open Crown Temperature - Port 2 (PV)
7522 Open Crown Temperature - Port 4 (PV)
7483 Open Crown Temperature - Port 6 (PV)
7525 Open Crown Temperature - Port 7 (PV)
7999 Outside Windspeed Anemometer
11105 Port 1 Combustion Air Flow LHS (OP)
11111 Port 2 - 3 Combustion Air Flow LHS (OP)
8390 Port 5 Gas Flow (PV)
6585 Port 6 Gas Flow (PV)
7667 Port 7 Gas Flow (PV)
11221 Services Building MCC1 - MV67
11217 Services Building MCC9 Cat B Supply - MV60
8344 Total CCCW Flow Measurement
136 Total Combustion Air Flow Measurement
135 Total Firm Gas Flow Measurement
9282 Tweel Position
30060 U S Flowing End Air Flow Measurement
11384 Wobbe Index (Incoming Gas)
Online linear regression eliminating non-relevant tags

## Slide 21
Online linear regression eliminating non-relevant tags
Pipeline | Av. RMSE
1 | 4.59
2 | 4.70
3 | 4.31
4 | 4.30
5 | 4.31
6 | 4.50
7 | 4.27
8 | 4.25
9 | 4.18

## Slide 22
To-do (short-term)
Need bespoke filtering for some of the signals (we can do this with an extra column in the spreadsheet).
Establish and implement strategy for processing data that is affected by reversals.
Run the pre-processing tasks defined in the flow chart with the 168 inputs specified in the spreadsheet “UK5 AI Furnace Model Input Pre-Processing”.
To-do (longer-term)
Repeat analysis that use randomly selected inputs and/or randomly selected time lags.
Consider using a multi-output linear regression.

## Slide 23
Time
Time
Time
Fault
Density
Tag 1
Tag 2
Lag 1
Lag 2
Multi-output linear regression

## Slide 24
Time
Time
Time
Fault
Density
Tag 1
Tag 2
Lag 1
Lag 2
Multi-output linear regression

## Slide 25
Time
Time
Time
Fault
Density
Tag 1
Tag 2
Lag 1
Lag 2
Multi-output linear regression (now including previous fault density)

## Slide 26
Time
Time
Time
Fault
Density
Tag 1
Tag 2
Lag 1
Lag 2
Multi-output linear regression (now including previous fault density)

## Slide 28
Constant
Previous fault density

## Slide 29
Constant
Previous fault density
The further from zero, the more important each input is. So high (absolute) values on the RHS of this matrix indicate that is important (for example).

## Slide 30
After batch training

## Slide 31
After batch training

## Slide 32
After batch training
Becomes less important as we look further into the future

## Slide 33
After batch training
Some inputs become increasingly important

## Slide 34
After batch training
Some inputs have a ‘time window’ where they are important

## Slide 35
Still some work to do…
Is currently ‘batch’, not online
Training lots of linear regression models currently isn’t equivalent to training the multi-output linear regression model; need to check this!
Does raise some difficult questions… What should we do with the time lags?
Could potentially optimise different models for predicting different lengths into the future (we’re good at 8 hours, but 4 hours needs improvement etc.)

## Slide 36
Conclusions
The reversals pre-processing strategy with the previous specified pre-processing tasks seems to outcome better quality of inputs and thus, better predictors.
Identifying non-relevant tags with the Linear Regression parameters and eliminating them, is still a good way to improve the predictive performance of the model.
Multi-output regression appears to have potential but further work still needed.

## Slide 37
Next activities
To-do (short-term)
Need bespoke filtering for some of the signals (we can do this with an extra column in the spreadsheet).
Run the pre-processing tasks defined in the flow chart with the 168 inputs specified in the spreadsheet “UK5 AI Furnace Model Input Pre-Processing”.
To-do (longer-term)
Repeat analysis that use randomly selected inputs and/or randomly selected time lags.
Consider using a multi-output linear regression.

## Slide 38: Thank you for your attention. ANY QUESTIONS?