## Slide 1: NSG Pilkington – University of Liverpool Machine Learning Project: 12/05/2021
Dr. Peter Green
Diego Echeverria
Sarini Jayasinghe
Risk Institute,
School of Engineering

## Slide 2
Today
Affect of signal processing on model performance
Regenerator Base and Regenerator Crown temperatures
Reversals
Combustion air flow
Mixture of Experts approach (if there’s time)

## Slide 3
Affect of Signal Processing on Model Performance
Unfortunately we’re seeing overfitting (very good fit to the training data but predictions on new data deteriorate).
Here is an example where the importance of one of the Regenerator Crown / Base temperature is ‘over emphasised’. The same happens regardless whether or not we include LHS / RHS differences.

## Slide 4
Affect of Signal Processing on Model Performance
We still get similar performance even just using the average of the Regenerator Crown and Regenerator Base temperatures (averaged across each port).
Perhaps because they are often correlated?
In fact, we can get better results by ignoring the Regenerator Crown and Regenerator Base temperatures completely (!)

## Slide 5
Read raw data and time lag
Data not found
Enable?
0
Isolate over time period
Inside Eng min-max?
False
Process data outside limits
1
True
Remove spikes?
1
Identify outliers (high pass filter)
Remove outliers
0
Reversals?
1
Reversal processing
0
Filtering?
1
0
Low pass filter
Interpolate
Extract values & time stamps
Combination?
1
0
Data Processing Pipeline (Standard)

## Slide 6
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Reversal processing
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Signal 1
Difference between 2 signals
Signal 2
Data Processing Pipeline (Regenerator Base and Regenerator Crown Temperatures)

## Slide 7
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Reversal processing
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Signal 1
Difference between 2 signals
Signal 2
Data Processing Pipeline (Regenerator Base and Regenerator Crown Temperatures)

## Slide 8
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Reversal processing
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Interpolate
Signal 1
Difference between 2 signals
Signal 2
Data Processing Pipeline (Regenerator Base and Regenerator Crown Temperatures)

## Slide 9
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Reversal processing
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Signal 1
Difference between 2 signals
Signal 2
Data Processing Pipeline (Regenerator Base and Regenerator Crown Temperatures)

## Slide 10
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Reversal processing
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Signal 1
Difference between 2 signals
Signal 2
Data Processing Pipeline (Regenerator Base and Regenerator Crown Temperatures)

## Slide 11
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Reversal processing
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Signal 1
Difference between 2 signals
Signal 2
Data Processing Pipeline (Regenerator Base and Regenerator Crown Temperatures)

## Slide 12: Reversals: before

## Slide 13: Reversals: we now have
Search for the minimum value of the signal at the first 40 minutes to identify the point at firing.
Capture the max value of the signal within a 40-minute time period

## Slide 14: Reversals
Search for the minimum value of the signal at the first 40 minutes to identify the point at firing.
Capture the max value of the signal within a 40-minute time period

## Slide 15: Reversals
Search for the minimum value of the signal at the first 40 minutes to identify the point at firing.
Capture the max value of the signal within a 40-minute time period

## Slide 16: Reversals

## Slide 17: Reversals: signals ready to be combined

## Slide 18: Inputs labeled for reversals conditioning (combine=0)
Zoom in
More zoom in

## Slide 19: Data Processing Pipeline (Combustion Air Flow)
Read raw data and time lag
Data not found
Isolate over time period
Remove spikes
Combine by taking max
Extract values & time stamps
Identify pair of tags to be combined
Low pass filter
Interpolate
Combined signal

## Slide 20: Combinations (Combustion Air Flow)

## Slide 21: Combinations (Combustion Air Flow)

## Slide 22: Combinations (Combustion Air Flow)

## Slide 23: Combinations (Combustion Air Flow)

## Slide 24: Combinations (Combustion Air Flow)

## Slide 25
Mixture of Experts Approach
(Using the previous week’s PCA plot as an example.)
As we move between different states, we have different optimal parameters for the model.
Currently, after we move between states, the model needs to spend some time retuning its parameters.
We originally suggested a model with time-varying parameters because we know that the furnace will change over time (degradation etc.)
But the PCA analysis shows that there are more severe, shorter-term changes in state as a result of product changes.
There isn’t a single linear model that can perform well over all of the different products.

## Slide 26
Mixture of Experts Approach
(Using the previous week’s PCA plot as an example.)
Mixture of experts; we have different models that represent different regions of the state-space.
When making predictions, each expert gets a ‘vote’ (between 0 and 1).
The final prediction is then made by weighting the predictions of each expert according to their vote:
Expert 1
Expert 2

## Slide 27
Mixture of Experts Approach
(Using the previous week’s PCA plot as an example.)
Mixture of experts; we have different models that represent different regions of the state-space.
When making predictions, each expert gets a ‘vote’ (between 0 and 1).
The final prediction is then made by weighting the predictions of each expert according to their vote:
Expert 1
Expert 2

## Slide 28
Mixture of Experts Approach
(Using the previous week’s PCA plot as an example.)
Mixture of experts; we have different models that represent different regions of the state-space.
When making predictions, each expert gets a ‘vote’ (between 0 and 1).
The final prediction is then made by weighting the predictions of each expert according to their vote:
Expert 1
Expert 2

## Slide 29
Mixture of Experts Approach
(Using the previous week’s PCA plot as an example.)
Mixture of experts; we have different models that represent different regions of the state-space.
When making predictions, each expert gets a ‘vote’ (between 0 and 1).
The final prediction is then made by weighting the predictions of each expert according to their vote:
Expert 1
Expert 2